## Slide 1: Development of an Acoustic Tension Cable Damage Localization Package
Smith, Cressman, Baima, Morano, Pickering
Vincent , Hu
OCE 495- Senior Design

## Slide 2: Contents
Introduction
Problem Statement
Concept Generation
Project Focus
Phase 1: Frequency Identification
  Objectives
  Experimental Modal Analysis
    Methods
    Results
  Newport Bridge Modal Analysis
    Theoretical Modal Analysis of Newport Bridge
    Selection of Driving and Listening frequencies
Phase 2: Design and Application of Active System
  Objectives
  Design of active sensor package
  Application of Package to Bridge
    Application of package to Newport Bridge
    Preliminary readings and results
Results of project
Conclusions
Acknowledgements

## Slide 3: Introduction
Large scale structures such as bridges are a vital component of transportation in developed countries. These structures require specific and careful maintenance to ensure the safety of the public that use them. The term structural health monitoring (SHM) refers to the process of identifying and mitigating damage to engineering structures. A particularly relevant example is the main cable bundles on Suspension bridges. Over time individual cables in the main bundles will corrode and snap. Current SHM methods for monitoring the health of these cables is costly and time intensive:
    A current visual inspection method of a 10ft length of cable, wedging down 5 inches at 8 points around the circumference, only exposes one side of 4000 linear feet of weave, or 0.007% of the total length. (study on the Bear Mountain Bridge)
    Current exposure process can cost in the order of $2 million to expose, inspect, and reinstate ~320 ft of cable.

## Slide 4: Problem Statement
Using the Claiborn Pell Bridge as a test bed, acoustic monitoring of suspension cables will be explored as a viable replacement to current inspection methods.
Acoustic monitoring holds the potential to locate precisely where a cable snap occurs and which cable failed.
By implementing an active acoustic sensor package on the bridge, it is hoped that cable failure localization can be done while greatly reducing cost and labor involved.

## Slide 5: Concept Generation
Following a Literature and Patent Search it was decided to use an active system
Examples of Passive systems were found; however, wired systems tended to be costly and wireless systems had the large hurdle of time synchronization
The active system benefited from being close to a power source, needing minimal wiring and did not need time synchronization
The active system was considered to work off the idea of reflectometry.
Breaks, snaps, and wearing of the cable will all have effects on the propagation time of sound in the suspension cables
By using a sensor package to inject a measured signal and listening to its return, it is hoped that structural damage can be located both in the length of the structure and specific cable

## Slide 6: Project Focus
The Project is split over two semesters, or two phases
  Phase 1: Frequency Identification
    It is important to consider which frequencies have the greatest ability to travel the long distances of the bridge.
    It is necessary to consider how the grouping and clamping of the wires found on the bridge will affect the frequencies propagating down the line.
    In phase 1, an experimental study was completed to determine the most viable frequencies to drive the sensors with
  Phase 2: System Design and Application
    An active sensor package was developed to send acoustic signals down the suspension cables
    The system was applied to both an in house test bed and the Newport/Pell Bridge
    Results were gathered and Analysed

## Slide 7: Phase 1: Frequency Analysis Objectives
In order to select the correct frequencies to drive the sensor package, experiments were undertaken in house to see how sound propagated down the cable
The objectives of the experiments were as followed:
  Acoustic Impulses were sent down steel of similar gauge and type to determine the resonant frequencies and compare them to theoretically calculated frequencies. Experiment was done for fixed and unfixed
  The experiment was repeated with the wire grouped, clamped, and group/clamped to see how the fundamental frequencies were altered
  Group/Clamped wire was cut. The wire was then driven and the resulting impulse was identified
  By analyzing the results, the frequency and sample rate for the package were determined.

## Slide 8: Phase 1: Frequency Determination In House experimentation
Free Hanging tests:
  Setup:
    Wire suspended by rubber bands
    Piezoelectric sensors placed at end of wire
    Microphones placed at intervals along wire
  Testing Procedure:
    Using a Hammer, the rod was struck at its end to create transverse and longitudinal acoustic events
    The loud acoustic event was recorded by both the microphones and piezo sensor
    Fourier and Prony Analysis were conducted to determine dominant frequencies
    Frequencies were compared to the modal analysis